## Slide 1: 硒化镉量子点的二维光谱探测
答辩人：陈稼霖
导师：John A. McGuire
专业：物理学
2021 年 6 月 1 日

## Slide 2: Background
Our case: two pump pulse -
probe pulse –
collect signal in direction
Four-wave mixing

## Slide 3: Experiment Setup
Laser Source
(Light Conversion Inc, CARBIDE - CB3)
Center wavelength ~ 1030 nm
Repetition freq 100 kHz
Power 40 W
Notes: 如图为我们使用的2D光谱测量系统. 我们的激光源产生中心波长约 1030 nm，重复频率 100 kHz，总功率 40 W 的超快激光脉冲输出.

## Slide 4: Experiment Setup
OPA (Light Conversion, ORPHEUS-TWINS)
Input 1030 nm
Output 1292 nm
1mm BBO
1292 nm 464 nm
Notes: 输出后被分束镜分为两束，其中一束输入声光调制器（简称OPA）后波长转换为 1292 nm，再经 1 mm BBO 晶体通过二次谐波产生将波长转换为 464 nm.

## Slide 5: Experiment Setup
Pulse shaper
(PhaseTech, QuickShape Visible)
Chop mode
phase cycling mode
  Divide one pulse into two
  RF power adjustment
  Phase adjustment
  Delay scan
Notes: 利用脉冲整形器（虚线方框 I）可以将输入的脉冲调制为我们所需的序列。在脉冲整形器中，脉冲经反射光栅反射而将不同波长的成分散开，再经离轴抛物面镜的反射而变为平行光，通过高速任意波形发生器驱动 AOM 中的压电陶瓷可以将。脉冲整形器具有两种工作模式，一种是 chop mode，在 chop mode 下，脉冲整形器控制输入的两个相邻脉冲，使它们一个通过，一个不通过，另一种是 phase cycling mode，在 phase cycling mode 下，脉冲整形器可以将一个脉冲在时域上一分为二，并且调节脉冲的能量、相位和两个脉冲间的时延。

## Slide 6: Experiment Setup
Long travel stage
(Thorlabs, LTS300)
Provide pump-probe delay
4mm YAG
1030 nm 515nm
Notes: 如图为我们使用的2D光谱测量系统. 我们的激光源产生中心波长约 1030 nm，重复频率 100 kHz，总功率 40 W 的超快激光脉冲输出.

## Slide 7: Experiment Setup
Spectrometer
(北京卓立汉光, Omni-200i)
CMOS Monochrome LineScan Sensor
(Teledyne e2v, OCTOPLUS BA2)
Notes: 如图为我们使用的2D光谱测量系统. 我们的激光源产生中心波长约 1030 nm，重复频率 100 kHz，总功率 40 W 的超快激光脉冲输出.

## Slide 8: Experiment Setup
Sample: CdSe quantum dots
Notes: 如图为我们使用的2D光谱测量系统. 我们的激光源产生中心波长约 1030 nm，重复频率 100 kHz，总功率 40 W 的超快激光脉冲输出.

## Slide 9: Experiment Setup
Spectrum of pump and probe
(With absorption spectrum of sample for comparison)
Notes: 如图为我们使用的2D光谱测量系统. 我们的激光源产生中心波长约 1030 nm，重复频率 100 kHz，总功率 40 W 的超快激光脉冲输出.

## Slide 10: Estimation: Single-exciton regime?
Molar extinction coefficient[2]:
Scattering cross section[2]:
[2] JASIENIAK J, SMITH L, VAN EMBDEN J, et al. Re-examination of the size-dependent absorption properties of CdSe quantum dots[J]. The Journal of Physical Chemistry C, 2009, 113(45): 19468–19474.
Detector:
50 W
Rf power
= 20 %
Wavelength
= 640 nm
Photon fluence:

## Slide 11: Estimation: Single-exciton regime?
Photon # absorbed per dot per pulse:
Photon fluence Scattering cross section = 0.113
Poison distribution of photon # absorbed:
Single-exciton regime

## Slide 12: Transient Absorption
I() = I(chop off, ) – I(chop on, )
(Odd and even frame signal processed separately)
Notes: 如图为我们使用的2D光谱测量系统. 我们的激光源产生中心波长约 1030 nm，重复频率 100 kHz，总功率 40 W 的超快激光脉冲输出.

## Slide 13: Transient Absorption
I() = I(chop off, ) – I(chop on, )
Scan T from -100 ps to 500 ps
Notes: 如图为我们使用的2D光谱测量系统. 我们的激光源产生中心波长约 1030 nm，重复频率 100 kHz，总功率 40 W 的超快激光脉冲输出.

## Slide 14: Transient Absorption
I() = I(chop off, ) – I(chop on, )
T = 1.8 ps
Notes: 如图为我们使用的2D光谱测量系统. 我们的激光源产生中心波长约 1030 nm，重复频率 100 kHz，总功率 40 W 的超快激光脉冲输出.

## Slide 15: 2D Spectrum
I() = I(phase 0, phase 0, ) - I(phase , phase , )
+ I(phase , phase , ) - I(phase 0, phase , )
(Even and odd frames processed separately)
Notes: 如图为我们使用的2D光谱测量系统. 我们的激光源产生中心波长约 1030 nm，重复频率 100 kHz，总功率 40 W 的超快激光脉冲输出.

## Slide 16: 2D Spectrum
ps
①: pump at 1S3/2 1S(e), probe at 1S3/2 1S(e)
②: pump at 1S3/2 1S(e), probe at 2S3/2 1S(e)
③: pump at 1S3/2 1S(e), probe at 1P3/2 1P(e)
①
②
③

## Slide 17: 2D Spectrum
ps
ps
ps

## Slide 18: Acknowledgement: Our Team
John A. McGuire
Associate Professor
(second from right)
Chaoyi Liang
B.S. University of Shanghai for Science and Technology
2019-present
(first from right)
Qingyu Wang
Undergraduate, ShanghaiTech University
2017-present
(first from left)
Jialin Chen
Undergraduate, ShanghaiTech University
2017-present
(second from left)

## Slide 19
Thank you for listening!